## Slide 1: 3 - IBAMR Associated Files (.vertex, .spring, etc)

## Slide 2: Learning IBAMR
Download:
  https://github.com/IBAMR/IBAMR
General info about the immersed boundary method:
  http://math.nyu.edu/faculty/peskin
Source code documentation:
  http://ibamr.github.io/IBAMR/ibamr/html/
Wiki:
  https://github.com/IBAMR/IBAMR/wiki
Frequently asked questions:
  https://github.com/IBAMR/IBAMR/wiki/FAQ
Support for IBAMR is available via the IBAMR Users Google Group (ibamr-users@googlegroups.com). Discussion related to the continued development of IBAMR is via the IBAMR Developers Google Group (ibamr-dev@googlegroups.com).

## Slide 3
What do the different input files do?
The input2d/3d files include a lot of information on physical parameters (density, viscosity, boundary conditions, domain size) and numerical parameters (dt, dx, printing intervals, etc.)
In addition to the input2d/input3d files, there are a number of files that specify the initial conditions and material properties of the immersed elastic structures.
The only such file that is required is the ".vertex" file, which specifies the initial positions of the IB points.
There are several additional files that may be optionally specified:
    A ".spring" file can be used to specify an essentially arbitrary network of linear or nonlinear springs that connect the various IB points. Each "spring" connects precisely two IB points.
    A ".beam" file can be used to specify a collection of linear beams with a preferred curvature. Each "beam" connects precisely three IB points.
Input files
Notes: *

## Slide 4: Input files cont’d
A ".target" file is used to specify IB points that are, by default, "tethered" by stiff linear springs to their initial positions. Note that it is also possible to update the location to which each target point is tethered to within a simulation, so as to provide an approximately-prescribed motion for the target points. (See below.)
A ".anchor" file is used to specify "anchor" points. In IBAMR, anchor points are IB points that neither apply force to the fluid nor interpolate velocity from the fluid. They are literally anchored in place. (Note: Anchor points are distinct from target points. Target points can be thought of as being tethered to anchor points.)
A ".mass" file is used to specify any additional mass associated with the IB points. For such files to have any effect, it is necessary that the IB solver be run in "penalty-IB" mode.

## Slide 5
Vertex file format
Vertex input files end with the extension ".vertex" and have the following format for two-dimensional models:
N # number of vertices in the file
x_0 y_0 # (x,y)-coordinates of vertex 0
x_1 y_1 # (x,y)-coordinates of vertex 1
...
x_{N-1} y_{N-1} # (x,y)-coordinates of vertex N-1
Vertex input files end with the extension ".vertex" and have the following format for three-dimensional models:
N # number of vertices in the file
x_0 y_0 z_0 # (x,y,z)-coordinates of vertex 0
x_1 y_1 z_1 # (x,y,z)-coordinates of vertex 1
...
x_{N-1} y_{N-1} z_{N-1} # (x,y,z)-coordinates of vertex N-1

## Slide 6
Spring file format
Spring input files end with the extension ".spring" and have the following format:
M # number of links in the file
i_0 j_0 kappa_0 length_0 fcn_idx_0
# first vertex index, second vertex index, spring constant,
# rest length, spring function index
i_1 j_1 kappa_1 length_1 fcn_idx_1
i_2 j_2 kappa_2 length_2 fcn_idx_2
...
Note:
  There is no restriction on the number of springs that may be associated with any particular node of the Lagrangian mesh.
  The rest length and force function index are optional values. If they are not provided, by default the rest length will be set to the value 0.0 and the force function index will be set to 0. This corresponds to a linear spring with zero rest length.

## Slide 7
Beam file format
Beam input files end with the extension ".beam" and have the following format:
M # number of beams in the file
i_0 j_0 k_0 kappa_0
# first vertex index, second vertex index, third vertex index,
# bending rigidity
i_1 j_1 k_1 kappa_1
# first vertex index, second vertex index, third vertex index,
# bending rigidity
i_2 j_2 k_2 kappa_2
# first vertex index, second vertex index, third vertex index,
#bending rigidity ...

## Slide 8
Target point file format
Target point input files end with the extension ".target" and have the following format:
M # number of target points in the file
i_0 kappa_0 eta_0
# vertex index, penalty spring constant, penalty damping coefficient
i_1 kappa_1 eta_1
i_2 kappa_2 eta_2
...
Note:
  Target points are anchored to their initial positions by linear springs with the specified spring constants and with zero resting lengths. Consequently, target points approximately enforce internal Dirichlet boundary conditions. The penalty parameter provides control over the energetic penalty imposed when the position of the Lagrangian immersed boundary point deviates from that of its specified fixed location.
  Damping coefficients are optional and are set to 0.0 if not supplied. Target points are "anchored" in place using Kelvin-Voigt viscoelastic elements.

## Slide 9
Mass point file format
Mass point input files end with the extension ".mass" and have the following format:
M # number of mass points in the file
i_0 mass_0 kappa_0 # vertex index, point mass, penalty spring constant
i_1 mass_1 kappa_1
i_2 mass_2 kappa_2
...
Note:
  Mass points are anchored to "ghost" massive particles by linear springs with the specified spring constants and with zero resting lengths. The massive particles are "isolated" and simply move according to Newton's laws. The penalty parameter provides control over the energetic penalty imposed when the position of the Lagrangian immersed boundary point deviates from that of its massive copy.

## Slide 10: Rubber band example
An example is available on github:
  3-Example_2Drubber_band
The MATLAB code creates the .vertex and .spring files for a rubber band that resists stretching.

## Slide 11: HW - Your own rubber band
Modify the rubber band example.
  Write your own generate_mesh.m file that puts down .vertex points and .springs.
  Make the rubber band 50% smaller and deform it initially in a different way.

## Slide 12: generate_mesh2d.m
L = 1; % length of computational domain (m)
N = 512; % number of Cartesian grid meshwidths at the finest level of the AMR grid
dx = L/N; % Cartesian mesh width (m)
radius = 0.1; % radius of band (m)
epsilon = 0.005; % deformation in the x-direction
band_length = 2*pi*radius; % rubber band length (m)
npts = ceil(2*(band_length/L)*N); % number of points along the rubber band
ds = band_length/(npts); % physical distance between neighboring Lagrangian mesh points (m)
dtheta = 2*pi/npts;
mesh_name = 'rubber_band_'; % structure name
kappa_spring = 2.0e3; % spring constant (Newton)
kappa_beam = 5.0e-3; % beam stiffness constant (Newton m^2)

## Slide 13: Generate_mesh2d.m .vertex
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% Write out the vertex information
vertex_fid = fopen([mesh_name num2str(N) '.vertex'], 'w');
fprintf(vertex_fid, '%d\n', npts);
for s = 0:npts-1
X(1) = (radius+epsilon)*sin(s*dtheta);
X(2) = radius*cos(s*dtheta);
fprintf(vertex_fid, '%1.16e %1.16e\n', X(1), X(2));
end
fclose(vertex_fid);
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 14: rubber_band_512.vertex
644
0.0000000000000000e+00 1.0000000000000001e-01
1.0244161346221071e-03 9.9995240574191152e-02
2.0487347565924115e-03 9.9980962749807278e-02
3.0728583625411962e-03 9.9957167885933298e-02
4.0966894676620277e-03 9.9923858247566999e-02
5.1201306149911948e-03 9.9881037005403420e-02
6.1430843846844874e-03 9.9828708235533081e-02
7.1654534032904536e-03 9.9766876919053921e-02
8.1871403530192222e-03 9.9695548941597226e-02
9.2080479810060564e-03 9.9614731092767334e-02
1.0228079108568690e-02 9.9524431065495328e-02
1.1247136640457638e-02 9.9424657455306847e-02
1.2265123574098539e-02 9.9315419759503781e-02
1.3281943008825695e-02 9.9196728376260312e-02
1.4297498155105894e-02 9.9068594603633084e-02
1.5311692343751664e-02 9.8931030638485795e-02
1.6324429035123069e-02 9.8784049575328159e-02
1.7335611828317186e-02 9.8627665405069495e-02
1.8345144470344348e-02 9.8461893013686907e-02

## Slide 15: Generate_mesh2d.m .spring
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% Write out the spring information
spring_fid = fopen([mesh_name num2str(N) '.spring'], 'w');
fprintf(spring_fid, '%d\n', npts-1);
for s = 0:npts-2
fprintf(spring_fid, '%d %d %1.16e %1.16e\n', s, s+1, kappa_spring*ds/(ds^2), ds);
end
fclose(spring_fid);
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 16: rubber_band_512.spring
643
0 1 2.0499156670236122e+06 9.7564989241919039e-04
1 2 2.0499156670236122e+06 9.7564989241919039e-04
2 3 2.0499156670236122e+06 9.7564989241919039e-04
3 4 2.0499156670236122e+06 9.7564989241919039e-04
4 5 2.0499156670236122e+06 9.7564989241919039e-04
5 6 2.0499156670236122e+06 9.7564989241919039e-04
6 7 2.0499156670236122e+06 9.7564989241919039e-04
7 8 2.0499156670236122e+06 9.7564989241919039e-04
8 9 2.0499156670236122e+06 9.7564989241919039e-04
9 10 2.0499156670236122e+06 9.7564989241919039e-04
10 11 2.0499156670236122e+06 9.7564989241919039e-04
11 12 2.0499156670236122e+06 9.7564989241919039e-04
12 13 2.0499156670236122e+06 9.7564989241919039e-04
13 14 2.0499156670236122e+06 9.7564989241919039e-04
14 15 2.0499156670236122e+06 9.7564989241919039e-04
15 16 2.0499156670236122e+06 9.7564989241919039e-04
16 17 2.0499156670236122e+06 9.7564989241919039e-04
17 18 2.0499156670236122e+06 9.7564989241919039e-04
18 19 2.0499156670236122e+06 9.7564989241919039e-04
19 20 2.0499156670236122e+06 9.7564989241919039e-04
20 21 2.0499156670236122e+06 9.7564989241919039e-04